## Slide 1
Center Wafer Distance Calculation for Reticles and Dies
Integration of MaskTooling Data into DMPT
Project context: DMPT distance enrichment | Presenter: Kevin Su | September 1, 2026
(0,0)
reticle shot
wafer
die array
Notes: Open with the practical purpose: DMPT has the target field but not the computed value.
Frame the hierarchy visually: wafer center is the origin; reticles contain dies; both need center-distance values.
Transition: the business question is how to populate the field reliably from existing data.
[Sources]
User-provided project brief and requested presentation content.

## Slide 2
BUSINESS NEED
DMPT needs an automated distance value
02
DMPT field
center_mm_distance
Currently not populated
MaskTooling
physical layout data
Calculation
reticle + die distance
DMPT
populated field
Objective
Calculate distance from reticle center to wafer center
Calculate distance from die center to wafer center
Populate the DMPT value automatically
Notes: State the data product need clearly: the field exists, but automation is missing.
The workflow should consume MaskTooling data, compute physical distances, and write the result into DMPT.
Emphasize that the same conceptual distance is needed at reticle and die granularity.
[Sources]
User-provided project brief and requested presentation content.

## Slide 3
INITIAL INVESTIGATION
The key decision was how to derive coordinates
03
Option 1
Reconstruct coordinates
Option 2
Use stored physical coordinates
Inputs: reticle index, die index, pitch values
Risk: rebuilds layout logic outside the source system
Inputs: shotX, shotY, X, Y
Advantage: uses source-of-record coordinates directly
Challenge: choose the approach that is most reliable and maintainable
Notes: Explain that the investigation started with two technically plausible paths.
Option 1 is mathematically possible, but it recreates assumptions about layout and pitch.
Option 2 is preferable if MaskTooling already stores coordinates referenced to wafer center.
[Sources]
User-provided project brief and requested presentation content.

## Slide 4
DATABASE EXPLORATION
MaskTooling exposes reticle and die geometry
04
waferShots
waferDie
Reticle information
shotX
shotY
col
row
Die information
X
Y
sizeX
sizeY
diameter_mm
MaskTooling
layout source
Notes: Walk through the two main MaskTooling structures analyzed.
waferShots carries reticle-level coordinates and grid identifiers; waferDie carries die-level coordinates and size information.
This sets up the discovery: the needed physical coordinates are present before we calculate anything.
[Sources]
User-provided project brief and requested presentation content.

## Slide 5
KEY DISCOVERY
Coordinates are already centered on the wafer
05
(0,0)
shotX, shotY
shotX, shotY
X,Y
Values cluster around a shared origin
Reticle coordinates: shotX, shotY
Die coordinates: X, Y
Observation: coordinates appear referenced to wafer center
Conclusion: no need to rebuild from indices
Use physical coordinates as the source of truth
Notes: This is the main finding: the coordinate system seems already centered around wafer origin.
That changes the implementation from reconstructing geometry to applying a distance formula to existing physical coordinates.
Call out that this still needs validation against known examples, but it materially simplifies the design.
[Sources]
User-provided project brief and requested presentation content.

## Slide 6
PROPOSED CALCULATION
Euclidean distance converts coordinates into center distance
06
(0,0)
distance vector
Reticles
Dreticle = sqrt(shotX^2 + shotY^2)
Dies
Ddie = sqrt(X^2 + Y^2)
If coordinates are micrometers:
Distance(mm) = Distance / 1000
Notes: Tie the visual to the formula: once the origin is wafer center, distance is the vector length from origin to the coordinate pair.
Use shotX and shotY for reticles; use X and Y for dies.
Confirm coordinate units in implementation. If stored in micrometers, divide by 1000 before writing millimeters.
[Sources]
User-provided project brief and requested presentation content.

## Slide 7
DATA MAPPING
Device identifiers connect DMPT to MaskTooling
07
DMPT.t_ret
DMPT.t_emap
device_id
deviceNames
deviceNumber
XF70649.1A
Finding: matching device identifiers exist in both systems
Notes: Explain the cross-system join path: DMPT reticle records map through emap to a device identifier.
MaskTooling has corresponding device names and device numbers.
Use the example identifier to make the mapping tangible for the audience.
[Sources]
User-provided project brief and requested presentation content.

## Slide 8
OPEN POINT
One mapping point remains before implementation
08
Validate
DMPT ret_x / ret_y
Compare with
MaskTooling col / row
Match confirmed?
Use shotX / shotY
Resolve index convention
Once validated: Reticle -> Coordinates -> Distance calculation -> Update center_mm_distance
Notes: Keep this slide focused on the remaining validation, not a new technical uncertainty.
The open point is whether DMPT ret_x and ret_y align directly with MaskTooling col and row.
Once that is confirmed, the reticle distance workflow can proceed directly from coordinates to update.
[Sources]
User-provided project brief and requested presentation content.

## Slide 9
TARGET ARCHITECTURE
The target workflow is a direct data enrichment path
09
DMPT.t_ret
DMPT.t_emap
device_id
deviceNames
waferShots
shotX / shotY
Euclidean distance
center_mm_distance
DMPT domain
MaskTooling domain
Calculation + update
Implementation principle: preserve the physical coordinate source, then calculate once in the enrichment layer.
Notes: Present the end-to-end target architecture as a simple enrichment pipeline.
The workflow starts in DMPT, resolves the device identity in MaskTooling, reads reticle coordinates, calculates Euclidean distance, and writes center_mm_distance.
The same pattern can be extended for dies using waferDie X and Y.
[Sources]
User-provided project brief and requested presentation content.

## Slide 10
CONCLUSION
A simpler path is ready for validation and build
10
Achievements
Coordinates already available in MaskTooling
Euclidean distance formula identified
Device mapping discovered
Validate mapping
next
Extract data
planned
Calculate
planned
Populate DMPT
target
Expected outcome
Reliable and automated center wafer distance calculation for reticles and dies.
Notes: Close by resolving the story: the investigation found that physical coordinates are already available, so the implementation can be simpler and more accurate.
The immediate next step is validating ret_x and ret_y against col and row.
After validation, implement extraction, calculate the distance values, and populate DMPT automatically.
[Sources]
User-provided project brief and requested presentation content.